## Slide 1
BARCODE & QR CODE
SCANNER
Project 3 · Detection · Localization · Decoding
Akoudad Karim · 126406 · UIR · Spring 2026

## Slide 2
UIR · Intro to Computer Vision · Spring 2026
Overview
Pipeline — 7 Steps
1
Grayscale
Lec 2
2
Gaussian Blur
Lec 2
3
Morph. Gradient
Lec 4
4
Otsu Threshold
Lec 4
5
Morph. Close
Lec 4
6
Contour Analysis
Lec 9
7
Decode
Lec 2/4
Linear Filtering (Lec 2)
Non-Linear / Morph. (Lec 4)
Boundary Detection (Lec 9)
Decoding
SAY: The full pipeline: image in, annotated detections out. 7 steps, all classical CV — no neural networks.

## Slide 3
UIR · Intro to Computer Vision · Spring 2026
Steps 1–2 · Lecture 2: Linear Filtering
Grayscale + Gaussian Blur
Preprocessing — denoise before edge detection
Grayscale
BGR tensor → single channel. Color is irrelevant for bar detection.
Gaussian Blur
Convolve with 5×5 Gaussian kernel. Suppresses noise before gradient ops.
Why blur first?
Derivatives amplify noise. Blur first = cleaner edges downstream.
def to_gray(img):
return cv2.cvtColor(
img, cv2.COLOR_BGR2GRAY)
def gaussian_blur(gray, ksize=5):
return cv2.GaussianBlur(
gray, (ksize, ksize), 0)
→ screenshot: cells gray + blurred side by side
SAY: First two steps are pure linear filtering from lecture 2. Gaussian blur is convolution — same math as the course.

## Slide 4
UIR · Intro to Computer Vision · Spring 2026
Steps 3–5 · Lecture 4: Non-Linear Filtering
Morphological Pipeline
Gradient → Threshold → Close
3 — Morph. Gradient
dilate(I,K) − erode(I,K)
Edge-like response. 9×3 kernel → emphasizes vertical bar transitions.
morphological_gradient(blurred)
→ screenshot: step result
4 — Otsu Threshold
minimize intra-class variance
Auto-selects optimal threshold. No manual tuning needed.
otsu_threshold(gradient)
→ screenshot: step result
5 — Morph. Close
erode(dilate(I,K), K)
21×7 kernel bridges gaps between bars → solid blob per code.
morphological_close(binary)
→ screenshot: step result
SAY: Three non-linear ops from lecture 4. The close is the key — it merges all barcode bars into one solid blob.

## Slide 5
UIR · Intro to Computer Vision · Spring 2026
Step 6 · Lecture 9: Boundary Detection
Contour Analysis — Localization
Find candidate barcode regions from binary mask
1
cv2.findContours on binary mask → list of contours
2
Filter by area ≥ 1500 px² (removes noise blobs)
3
cv2.boundingRect → (x, y, w, h) per candidate
4
Draw bounding boxes on original image
def find_candidate_regions(mask,
min_area=1500):
contours, _ = cv2.findContours(
mask,
cv2.RETR_EXTERNAL,
cv2.CHAIN_APPROX_SIMPLE
)
regions = []
for c in contours:
if cv2.contourArea(c) >= min_area:
regions.append(
cv2.boundingRect(c))
return regions
→ screenshot: closed mask + bounding boxes on image
SAY: Lecture 9 — boundary detection. After morphological close, each code is a solid blob. We just extract its bounding box.

## Slide 6
UIR · Intro to Computer Vision · Spring 2026
Step 7 · Multi-Variant Decoding
Decoding — 5 Variants
pyzbar on multiple preprocessed versions
1
Raw BGR
—
2
Grayscale
Lec 2
3
Adaptive Threshold
Lec 4
4
Inverted Adaptive
Lec 4
5
Sharpened
Lec 2
Sharpening kernel (Lec 2 — linear convolution):
K = [[0,-1, 0],
[-1, 5,-1],
[0,-1, 0]]
sharpened = cv2.filter2D(gray, -1, K)
Why 5 variants? Real-world images have glare, shadows,
low contrast — one preprocessing rarely decodes all cases.
Results deduplicated by (data, type) pair
SAY: pyzbar wraps zbar, handles QR + EAN + Code128 etc. We run it 5 times with different preprocessing to maximize decode rate.

## Slide 7
UIR · Intro to Computer Vision · Spring 2026
Results
Detection Results
Synthetic test images — all decoded correctly
screenshot:
qr_test.png
QRCODE
https://uir.ac.ma
Decoded
screenshot:
barcode_test.png
EAN13
5901234123457
Decoded
screenshot:
combined_test.png
BOTH
QR + Barcode
Decoded
SAY: 100% on synthetic images. Multi-variant decoding handles real-world photos too — we'll demo that now.

## Slide 8
LIVE DEMO
colab.research.google.com → Run all → Upload image
1. Runtime → Run all
2. Scroll to cell 10
3. Upload a barcode/QR image
4. Click Scan